Pipe Beveling Machine

Operator’s manual

TABLE OF CONTENTS

PART 1       EQUIPMENT INSTRUCTION

PART 2       SAFETY INSTRUCTIONS

PART 3       MACHINE SPECIFICATION

PART 4       INSTALLATION AND OPERATION OF ISE SERIES

PART 5       INSTALLATION AND OPERATION OF ISY SERIES

PART 6       DIAGRAM OF BEVELING TOOL

PART 7       DIAGRAM OF EXPANDING BLOCK

PART 8       TROUBLE SHOOTING

PART 9       PARTS LIST AND EXPLODED VIEWS

PART 1  Equipment introduction

We supplies machines and equipment to diverse industries where process piping systems are essential to their operation but require divergent machine tool technology. From power and petrochemical to semiconductor, food and dairy, ours wide range of portable tools can be found on all pipe and tube types, sizes and wall thickness..

FEATURES:

EASY OPERATION

| • | Convenient "fail safe" on/off motor valve |
| --- | --- |
| • | Adjustable hand grip speed control |
| • | In-feed hand wheel with indices for precise measurement |
| • | Adjustable dual-key design makes tool feed easy, absorbs torque, reduces operator fatigue and increases safety |
| • | The design of miniaturization is suitable for the homework place of low-clearance more |

FAST SETUP

| • | Set up and operate from storage case to pipe in under 5 minutes |
| --- | --- |
| • | "Quick change" extension legs use captivated fasteners to mount firmly to mandrel |
| • | One adjustment, universal three-leg chuck automatically centers and squares the machine in pipe I.D. |
| • | Install or adjust tool bits in seconds |

TYPICAL FUNCTION DESIGN

| • | The main body made in aluminum alloy, which is quite light |
| --- | --- |
| • | Two bevel tools can be installed on rotary tool disk, pipe can be worked synchronously |
| • | The equipment can machining V and U groove |
| • | Use the ball slewing bearing and self-lubrication to prolong the equipment life |
| • | High strength mandrel and large-area expanding block mostly improve the rigidity |

PACKAGE

The machine is placed into a portable plywood case with expanding block, usual tool, beveling tools

PART 2  SAFTY INSTRUCTION

We take great pride in manufacturing safe, quality products. Please comply with the following safety rules and instructions when operating the equipment.

READ THE OPERATION MANUAL

Before installing, you should read the instruction of installation and operation, and then it can help you save time and avoid injuring the operator and the machines

INSPECT MACHINE & ACCESSORIES

Before installation, you should check the machine and its accessories. Look for worn

ALWAYS READ SIGNS AND LABLES

Please read the marks and signs. All the marks and signs should be clear and easy to read, and you should carefully to keep them.

DANGER! ELECTRIC SHOCK

Security of the electricity.

CAUTION INJURE HAND

Keep distance from rotating parts during operation.

WEAR SAFETY GOGGLE

Eye protection required. When using equipment, please wear safety goggle. No goggle no work

WEAR HEARING PROTECTION

When working near the equipment, it is better to wear some hearing protection device or other noise insulating facility

NO PUTTING ON GLOVES

It is unnecessary to ware gloves when operating the equipment. The beveling scraps should be cleaned by broom and dustpan to protect your hands from getting hurt

PART 3   MACHINE SPECIFICATION

Electric-Driven    ISE SERIES

| Model | ISE-30 | ISE -80 | ISE -159 | ISE -252 | ISE -252-2 | ISE -352 | ISE -352-2 | ISE -630 | ISE -630-2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Working range | ID | 18-25 | 28-76 | 65-159 | 80-240 | 80-240 | 150-330 | 150-330 | 300-600 | 300-600 |
|  | OD | 21-30 | 32-80 | 72-182 | 90-273 | 90-273 | 162-352 | 162-352 | 320-630 | 320-630 |
| Electric Motor Power | 800W | 1000W | 1200W |
| Power Supply | 220V 50HZ |
| Rotate Speed ( r/min) | 55 | 55 | 35 | 16 | 16 | 14 | 14 | 10 | 10 |
| Blade feed travel (MAX) | 35 | 55 | 50 | 55 | 55 | 55 | 55 | 55 | 55 |
| Beveling Thickness (mm) | 1.5-15 | 1.5-15 | 3-20 | 4-20 | 15-75 | 4-20 | 15-75 | 4-20 | 15-75 |
| Horizontal Blade Feed (r/mm) | - | - | - | - | 0.15 | - | 0.15 | - | 0.15 |
| Weight (KGS) | 10 | 11 | 22 | 32 | 40 | 53 | 57 | 103 | 99 |

Pneumatic-Driven   ISP SERIES

| Model | ISP-30 | ISP -80 | ISP -159 | ISP -252 | ISP -252-2 | ISP -352 | ISP -352-2 | ISP -630 | ISP -630-2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Working range | ID | 18-25 | 28-76 | 65-159 | 80-240 | 80-240 | 150-330 | 150-330 | 300-600 | 300-600 |
|  | OD | 21-30 | 32-80 | 72-182 | 90-273 | 90-273 | 162-352 | 162-352 | 320-630 | 320-630 |
| Air Motor Power | 450W | 580W | 800W |
| Air Pressure (MPa) | 0.6 | 0.7 | 0.9 | 1.0 |
| Rotate Speed ( r/min) | 55 | 55 | 35 | 16 | 16 | 14 | 14 | 10 | 10 |
| Blade feed travel (MAX) | 35 | 35 | 50 | 55 | 55 | 55 | 55 | 55 | 55 |
| Beveling Thickness (mm) | 1.5-15 | 1.5-15 | 3-20 | 4-20 | 15-75 | 4-20 | 15-75 | 4-20 | 15-75 |
| Horizontal Blade Feed (r/mm) | - | - | - | - | 0.15 | - | 0.15 | - | 0.15 |
| Weight (KGS) | 8 | 9 | 20 | 30 | 37 | 50 | 54 | 102 | 98 |

PART 4   INSTALLATION AND OPERATION OF ISE SERISE

Section I

- Measure the ID of the pipe, and then choose the proper expanding (swelling) block according to the diagram of expanding block chart, fixed them on the swell wedging block mechanism (expansion structure), and tighten the tension screw.

- According to the diagram of beveling tools, choose the proper one fixed on the blade disk (knife drum). Make sure the blade in clockwise. Caution: The blade can’t touch the principal axis; otherwise it may damage the equipment.

- Pulling back the travel of feed handwheel, there should be some space between the blade and the end of pipe. Insert the swell orientation mechanism (expansion structure) into the pipe, before tighten the pull rod screw, swing the equipment with hand, and make sure the equipment and the pipe are integrated. Caution: The expansion structure should not be inserting too deep, its better keep a 20mm distance between the work pieces

- Turn on the equipment, rotating the tool feed handwheel manually; make the blade edge keep in touch with the tube. The equipment start working

- After the blade installation is completed, the equipment can be moved and continue processing from one workpiece to another same specification workpiece, instead of adjusting the blade again, only pull back the travel of blade feed handwheel. Loosen the expansion nut, and fix it on another workpiece.

Section II

CORRECT OPERATING PROCESS OF BEVELING

  - Before beveling, please remove the rough edge and other incidentals after flame cutting with hammer. If the tube terminal surface is full of bumps and holes, the blade begin from the peak, and feed the blade carefully

  - When beveling, please add coolants (saponification oil) to prolong the tools life.

  - After beveling is completed, please back the blade disk by rotating the feed hand wheel in opposite direction.

  - If the blade is blunt, sharpen it or change one.

  - In order to ensure the beveling force, if the pipe wall thickness is above 20mm, you should bevel the pipe separately, first beveling the outside end, then beveling the inner part, or set a double blade to stagger the machining plane.

Section III

TRANSVERSE FEED OPERATION OF THE EQUIPMENT

(Suitable for ISE/ISP -252-2   ISE/ISP -352-2   ISE/ISP -630-2)

When bevel the pipe with angle 0°- 37°, it is achieved by this structure (transverse feed orient axle), the blade rest hold is supported by the locating axis, then choose the beveling angle, tighten the screws, therefore you can get a satisfying beveling angle, as for the structure, refer to diagram 4.

- Diagram 4 shows the vertical feed handle; first feed 3mm, second feed 3mm again. Note: Don’t adjust it when the equipment working

- Adjust vertical feed handle make cutter rise with the tube terminal surface keep proper distance to enter, turn on the equipment, no-load rotating start. After the cutter touches the peak of the tube, turn the equipment off. From the peak, make the cutter come down 3-4mm.

- Feed handwheel comes out to draw from outside entering, wave handwheel adjust the cutter touch the tube beveling plane, push the handwheel to the original position , then can start the machine and process beveling

- When pushing ring gear joggle the inside gear, the blade feed 0.15mm/circle automatically.

- When the ring gear is taken out, the inside gear is break away, the blade feed automatically stopped, rotate the quick feed handle manually, the blade can go in or go out of the tool holder (post) quickly so as to adjust and change the blade

- While installing in another tube and continue beveling, same operation with Section I

- After beveling is achieved, rise the vertically feed handwheel first, and then loosen the tension screw

- Other operation is carried out according to the above process.

- When beveling the pipe with small diameter, you can use a bench vise or clamp to fasten the pipe.

PART 5   INSTALLATION AND OPERATION OF ISP SERIES

Section I

CORRECT OPERATION PROCESS

- Take out the fast joint, fasten it on the air feeding tube (be ready for connecting the beveling machine)

- Choose the proper expanding block according the ID of the pipe, and install them on the expansion structure

- Fix the proper bevel tool on the knife drum

- Insert the expansion structure into the tube, make the equipment and tube are integrated

- Drip several drops of lubricating oil at the air entry joint

- Connect the equipment with the air compressor

- Turn on the air valve, and the equipment start work

- After beveling, rotate the handwheel in the opposite direction, back the knife drum(tool disk).Turn off the air valve, loosen the expansion handle unload the equipment

Section II

MAINTENANCE AND SAFETY TECHNOLOGY

- The compressed air required must be dehydrated and filtrated to prevent the parts rustiness

- When the beveling completed, add a little lubricating oil or antirust at the air entry joint

- When insert the equipment into the pipe, make sure keep distance between the beveling tool and working face

- When loosen the expansion screw (swelling nut), and take the equipment out or adjust the location of equipment, don’t make it slip into the pipe, otherwise will damage the bevel blade

- When rotating the blade feed handwheel, take care the connect joint between the blade and the uneven work face, keep the speed of blade feed, never feed the blade too fast

- During the feeding process (ISP), if the feed speed is too high to the air compressed air is too low so that the tool disk stop rotate, you should turn off the air valve, rotate the tool disk and the handwheel in opposite direction to let the blade rise, then you can continue the working. When the equipment’s working time reach 96 hours, you should add some lubricating oil or re-adjust and check it.

PART 6   DIAGRAM OF THE BEVEL TOOL

| Description | Part No. | Qty | Remark |
| --- | --- | --- | --- |
| Facing tool | 3712-01 | 1 | Beveling angle 0° |
| Bevel tool | 3712-02 | 1 | Beveling angle 30° |
| Bevel tool | 3712-03 | 1 | Beveling angle 37° |
| Inner bevel tool | 3712-04 | 1 | Beveling angle 15° |

Note:

The bevel tool set up for carbon steel pipe, if you want to bevel pipe made of stainless steel, alloy steel or cast steel, please contact us

PART 7   DIAGRAM OF THE EXPANDING BLOCK

(Swelling block / expansion part)

| Model | ISE/ISP-28 | ISE/ISP-80 | ISE/ISP -150 | ISE/ISP -252 | ISE/ISP -352 | ISE/ISP -630 |
| --- | --- | --- | --- | --- | --- | --- |
| No-Block |  | ￠28-36 | ￠65-87 | ￠80-100 | ￠150-180 | ￠300-330 |
| 306-1 | ￠18 | ￠36-44 | ￠87-105 | ￠100-120 | ￠180-210 | ￠330-360 |
| 306-2 | ￠19 | ￠44-52 | ￠105-123 | ￠120-140 | ￠210-240 | ￠360-390 |
| 306-3 | ￠20 | ￠52-60 | ￠123-141 | ￠140-160 | ￠240-270 | ￠390-420 |
| 306-4 | ￠21.5 | ￠60-68 | ￠141-159 | ￠160-180 | ￠270-300 | ￠420-450 |
| 306-5 | ￠23 | ￠68-76 |  | ￠180-200 | ￠300-330 | ￠450-480 |
| 306-6 | ￠24.5 |  |  | ￠200-220 |  | ￠480-510 |
| 306-7 | ￠26 |  |  | ￠220-240 |  | ￠510-540 |
| 306-8 | ￠27 |  |  |  |  | ￠540-570 |
| 306-9 |  |  |  |  |  | ￠570-600 |

PART 8   TROUBLE SHOOTING

| Trouble | Possible reason | Remedy |
| --- | --- | --- |
| Equipment doesn’t work | The wire isn’t connect well ; pneumatic actuator drive may have a entry problem | Check the wire and the air entry device to see if it is well installed |
| Pipe wave when working | The expansion structure isn’t fastened or the expanding block wrongly choose | Check the expansion screw or change a proper expanding block |
| Working face not good | The bevel tool is blunt or damaged | Change the bevel tool |

PART 9   PARTS LISTS AND EXPLODED VIEWS

ISP 30-80 AIR MOTOR

| NO. | NAME | QTY | NO. | NAME | QTY |
| --- | --- | --- | --- | --- | --- |
| 1 | Fast joint of air pipe | 1 | 15 | Bearing cover | 1 |
| 2 | Air entry-joint | 1 | 16 | Spring clamp-ring | 1 |
| 3 | Spring | 1 | 17 | Pin | 1 |
| 4 | Handle | 1 | 18 | Sound attenuator | 1 |
| 5 | Air valve body | 1 | 19 | Air motor casing | 5 |
| 6 | Steel ball | 1 | 20 | Lamina | 1 |
| 7 | Pin | 1 | 21 | Eccentricity bushing | 1 |
| 8 | Torsion spring | 1 | 22 | Bearing cover | 1 |
| 9 | Pressing pin | 1 | 23 | Deep-groove ball bearing | 1 |
| 10 | Pin | 1 | 24 | Gland ( pressing cover) | 3 |
| 11 | Air motor nut cover | 1 | 25 | Bolt M3X8 | 1 |
| 12 | Nut M8 | 1 |  |  |  |
| 13 | Air motor shaft | 1 |  |  |  |
| 14 | Deep-groove ball bearing | 1 |  |  |  |

ISP 159-630 AIR MOTOR

| NO. | NAME | QTY | NO. | NAME | QTY |
| --- | --- | --- | --- | --- | --- |
| 1 | Fast joint of air pipe | 1 | 15 | Deep-groove ball bearing | 1 |
| 2 | Ball valve switch | 1 | 16 | Bearing seat | 1 |
| 3 | Air motor cap | 1 | 17 | Cover | 1 |
| 4 | Nut M8 | 1 | 18 | Bolt M3X8 | 3 |
| 5 | Deep-groove ball bearing | 1 |  |  |  |
| 6 | Air motor bearing cover | 1 |  |  |  |
| 7 | Air motor internal part | 1 |  |  |  |
| 8 | Pin | 1 |  |  |  |
| 9 | Air motor bushing | 1 |  |  |  |
| 10 | O-shape loop | 1 |  |  |  |
| 11 | Air motor core | 1 |  |  |  |
| 12 | Muffle | 1 |  |  |  |
| 13 | Lamina | 5 |  |  |  |
| 14 | Plug-Head | 1 |  |  |  |

ISE-30 BEVELING MACHINE

| NO. | NAME | QTY | NO. | NAME | QTY |
| --- | --- | --- | --- | --- | --- |
| 1 | Bolt M4×12 | 4 | 35 | Second-class gear | 2 |
| 2 | Exhaust cover | 1 | 36 | Ball bearing | 1 |
| 3 | Cover | 1 | 37 | Deep-groove ball bearing-61904 | 3 |
| 4 | Deep-groove ball bearing-628 | 1 | 38 | Jump spring 39×16×1 | 1 |
| 5 | Bolt M4 | 1 | 39 | Third-class gear ring | 1 |
| 6 | Brush | 1 | 40 | Third-class planetary gear holder | 1 |
| 7 | Switch of electric motor | 1 | 41 | Third-class gear | 1 |
| 8 | Electric motor rotor | 1 | 42 | Ball bearing | 1 |
| 9 | Electric motor | 1 | 43 | Shell | 1 |
| 10 | Electric motor stator | 1 | 44 | Key | 1 |
| 11 | Bolt M4×12 | 1 | 45 | Needle roller bearing-6004 | 2 |
| 12 | Electric motor gasket | 1 | 46 | Gear | 1 |
| 13 | Bolt M4×12 | 4 | 47 | Tie bar | 1 |
| 14 | Deep-groove ball bearing-629 | 1 | 48 | Expansion bolt | 1 |
| 15 | Electric motor bearing holder | 1 | 49 | Bearing | 1 |
| 16 | Slanting gear Ø17.3 | 1 | 50 | Feed handwheel | 1 |
| 17 | Needle roller bearing 12×8×10 | 2 | 51 | Feed bolt cover | 1 |
| 18 | Slanting gear Ø37.8/ Ø28 | 2 | 52 | Feed handle | 4 |
| 19 | Output bearing | 1 | 53 | Up cover | 1 |
| 20 | Slanting gear Ø27.2 | 1 | 54 | Flexible gasket | 1 |
| 21 | Bolt M5×25 | 3 | 55 | Plane bearing | 1 |
| 22 | Deep-groove ball bearing-6001 | 2 | 56 | Key cover | 1 |
| 23 | Relaier | 1 | 57 | Bolt M6×30 | 4 |
| 24 | First-class gear ring | 1 | 58 | Deep-groove ball bearing-6006 | 2 |
| 25 | Jump spring | 1 | 59 | Bearing bushing block | 1 |
| 26 | First-class bushing block | 1 | 60 | Copper bush | 1 |
| 27 | Deep-groove ball bearing-16003 | 2 | 61 | Tool plate bearing | 1 |
| 28 | First-class planetary gear holder | 1 | 62 | Bolt M6×30 | 4 |
| 29 | First-class gear | 1 | 63 | Fimbriatum gear | 1 |
| 30 | Ball bearing | 1 | 64 | Gasket | 1 |
| 31 | Second-class gear ring | 1 | 65 | Down cover | 1 |
| 32 | Second-class bushing block | 1 | 66 | Tool plate | 1 |
| 33 | Deep-groove ball bearing-16004 | 1 | 67 | Expanding kep | 4 |
| 34 | Second-class planetary gear holder | 1 | 68 | Tie bar slanting bearing | 1 |

ISE-80 BEVELING MACHINE

| NO. | NAME | QTY | NO. | NAME | QTY |
| --- | --- | --- | --- | --- | --- |
| 1 | Bolt M4×12 | 4 | 37 | Deep-groove ball bearing-61904 | 3 |
| 2 | Exhaust cover | 1 | 38 | Jump spring 39×16×1 | 1 |
| 3 | Cover | 1 | 39 | Third-class gear ring | 1 |
| 4 | Deep-groove ball bearing-628 | 1 | 40 | Third-class planetary gear holder | 1 |
| 5 | Bolt M4 | 1 | 41 | Third-class gear | 1 |
| 6 | Brush | 1 | 42 | Ball bearing | 1 |
| 7 | Switch of electric motor | 1 | 43 | Shell | 1 |
| 8 | Electric motor rotor | 1 | 44 | Key | 1 |
| 9 | Electric motor | 1 | 45 | Needle roller bearing-6004 | 2 |
| 10 | Electric motor stator | 1 | 46 | Gear | 1 |
| 11 | Bolt M4×40 | 1 | 47 | Tie bar | 1 |
| 12 | Electric motor gasket | 1 | 48 | Expansion bolt | 1 |
| 13 | Bolt M4×12 | 4 | 49 | Bearing | 1 |
| 14 | Deep-groove ball bearing-629 | 1 | 50 | Feed handwheel | 1 |
| 15 | Electric motor bearing holder | 1 | 51 | Feed bolt cover | 1 |
| 16 | Slanting gear Ø17.3 | 1 | 52 | Feed handle | 4 |
| 17 | Needle roller bearing 12×8×10 | 2 | 53 | Up cover | 1 |
| 18 | Slanting gear Ø37.8/ Ø28 | 2 | 54 | Flexible gasket | 1 |
| 19 | Output bearing | 1 | 55 | Plane bearing | 1 |
| 20 | Slanting gear Ø27.2 | 1 | 56 | Key cover | 1 |
| 21 | Bolt M5×25 | 3 | 57 | Bolt M6×30 | 4 |
| 22 | Deep-groove ball bearing-6001 | 2 | 58 | Deep-groove ball bearing-6006 | 2 |
| 23 | Relaier | 1 | 59 | Bearing bushing block | 1 |
| 24 | First-class gear ring | 1 | 60 | Copper bush | 1 |
| 25 | Jump spring | 1 | 61 | Tool plate bearing | 1 |
| 26 | First-class bushing block | 1 | 62 | Bolt M6×30 | 4 |
| 27 | Deep-groove ball bearing-16003 | 2 | 63 | Fimbriatum gear | 1 |
| 28 | First-class planetary gear holder | 1 | 64 | Gasket | 1 |
| 29 | First-class gear | 2 | 65 | Down cover | 1 |
| 30 | Ball bearing | 1 | 66 | Tool plate | 1 |
| 31 | Second-class gear ring | 1 | 67 | Bolt M8×20 | 4 |
| 32 | Second-class bushing block | 1 | 68 | Sleeve | 1 |
| 33 | Deep-groove ball bearing-16004 | 1 | 69 | Expanding claw | 3 |
| 34 | Second-class planetary gear holder | 1 | 70 | Expanding block | 3 |
| 35 | Second-class gear | 2 | 71 | Spring | 2 |
| 36 | Ball bearing | 1 | 72 | Bolt M4×8 | 3 |

ISE-159 BEVELING MACHINE

| NO. | NAME | QTY | NO. | NAME | QTY |
| --- | --- | --- | --- | --- | --- |
| 1 | Cover | 1 | 44 | Third-class bearing | 1 |
| 2 | Deep-groove ball bearing | 1 | 45 | Gasket | 1 |
| 3 | Bolt | 4 | 46 | Deep-groove ball bearing | 1 |
| 4 | Switch of electric motor | 1 | 47 | Third-class gear | 1 |
| 5 | Cover of alternator | 1 | 48 | Needle roller | 1 |
| 6 | Bolt | 2 | 49 | Deep-groove ball bearing | 1 |
| 7 | Carbon brush | 1 | 50 | Third-class planetary gear frame | 1 |
| 8 | Carbon brush holder | 2 | 51 | Small gear | 1 |
| 9 | Electric motor casing | 2 | 52 | Copper bush | 1 |
| 10 | Electric motor rotor | 1 | 53 | Beveling tool bits | 1 |
| 11 | Bolt | 2 | 54 | Bolt | 3 |
| 12 | Electric motor stator | 1 | 55 | Tie bar | 1 |
| 13 | Cable | 1 | 56 | Sleeve | 1 |
| 14 | Deep-groove ball bearing | 1 | 57 | Expansion block screw | 6 |
| 15 | Electric motor gasket | 1 | 58 | Slanting screw | 3 |
| 16 | Key | 1 | 59 | Expansion block | 3 |
| 17 | Bolt | 4 | 60 | Slanting block | 3 |
| 18 | Needle roller bearing | 1 | 61 | Expansion block holder | 1 |
| 19 | Slanting gear bearing | 1 | 62 | Tool disk bolt | 8 |
| 20 | Electric motor frame | 1 | 63 | Tool disk | 1 |
| 21 | Slanting gear | 1 | 64 | Screw | 4 |
| 22 | Key | 1 | 65 | Cover | 1 |
| 23 | Slanting | 1 | 66 | Handle screw | 2 |
| 24 | Slanting | 1 | 67 | Needle roller bearing | 2 |
| 25 | Needle roller bearing | 1 | 68 | Deep-groove ball bearing | 1 |
| 26 | Delaier | 1 | 69 | Big gear | 1 |
| 27 | Deep-groove ball bearing | 2 | 70 | Machine body | 1 |
| 28 | Output bearing | 1 | 71 | Handle | 1 |
| 29 | First-class ring gear | 1 | 72 | Main bearing | 1 |
| 30 | Jump ring | 1 | 73 | Deep-groove ball bearing | 1 |
| 31 | First-class bushing block | 1 | 74 | Holder copper bush | 1 |
| 32 | Deep-groove ball bearing | 2 | 75 | Main bearing | 1 |
| 33 | First-class planetary gear holder | 1 | 76 | Crane service gear | 1 |
| 34 | First-class planetary gear | 1 | 77 | Holder | 1 |
| 35 | Needle roller | 1 | 78 | Bolt | 3 |
| 36 | Second-class gear ring | 1 | 79 | Bolt | 3 |
| 37 | Second-class bushing block | 1 | 80 | Plane bearing | 2 |
| 38 | Deep-groove ball bearing | 1 | 81 | Plane bearing holder | 1 |
| 39 | Second-class planetary gear | 1 | 82 | Feed handle | 1 |
| 40 | Needle roller | 1 | 83 | Jump ring | 1 |
| 41 | Second-class planetary gear holder | 1 | 84 | Feed handwheel | 1 |
| 42 | Jump ring | 1 | 85 | Thread casing | 1 |
| 43 | Deep-groove ball bearing | 1 | 86 | Expansion nut | 1 |

ISE-252/352/630-1 BEVELING MACHINE

| NO. | NAME | NO. | NAME |
| --- | --- | --- | --- |
| 1 | Cover | 43 | Second-class planetary gear holder |
| 2 | Deep-groove ball bearing | 44 | Deep-groove ball bearing |
| 3 | Bolt | 45 | Third-class ring gear |
| 4 | Switch | 46 | Machine casing |
| 5 | Bearing seat | 47 | Third-class planetary gear holder |
| 6 | Bolt | 48 | Key |
| 7 | Carbon brush | 49 | Roller bearing |
| 8 | Carbon brush holder | 50 | Spring ring for hole |
| 9 | Electric motor casing | 51 | Cone roller bearing |
| 10 | Electric motor rotor | 52 | Bolt |
| 11 | Blot | 53 | Lower cover of machine body |
| 12 | Electric motor stator | 54 | Tool disk |
| 13 | Cable | 55 | Main spindle bushing |
| 14 | Bearing | 56 | Roller bearing |
| 15 | Electric gasket | 57 | Spring ring for hole |
| 16 | Key | 58 | Bolt |
| 17 | Bolt | 59 | Main feed shaft |
| 18 | Slanting gear shaft | 60 | Pull-rod nut |
| 19 | Speed reducer | 61 | Expansion disk (nether) |
| 20 | Slanting gear wheel | 62 | Spring |
| 21 | Key | 63 | Slanting block |
| 22 | Slanting gear wheel | 64 | Spring |
| 23 | Slanting gear wheel | 65 | Expansion block (Expanding block) |
| 24 | Slanting gear wheel | 66 | Expansion disk (upper) |
| 25 | Bearing seat | 67 | Bevel tool |
| 26 | Bearing | 68 | Bolt |
| 27 | Bearing | 69 | Hanging ring |
| 28 | Output shaft | 70 | Handle |
| 29 | First-class bushing | 71 | Deep-groove ball bearing |
| 30 | First-class ring gear | 72 | Ring gear |
| 31 | Circlip | 73 | Machine post |
| 32 | Bearing | 74 | Thread bushing |
| 33 | Needle | 75 | Bolt |
| 34 | First-class planetary gear post | 76 | Cover |
| 35 | Deep-groove ball bearing | 77 | Feed handwheel |
| 36 | Needle | 78 | Handle |
| 37 | Second-class ring gear | 79 | Plane bearing |
| 38 | Second-class bushing | 80 | Bearing seat |
| 39 | Deep-groove ball bearing | 81 | Plane bearing |
| 40 | Deep-groove ball bearing | 82 | Bolt |
| 41 | Needle | 83 | Expansion Nut |
| 42 | Upper cover of machine body | 84 | Pull rod |

ISE-252-2 / 352-2 / 630-2 BEVELING MACHINE

| NO. | NAME | NO. | NAME | NO. | NAME |
| --- | --- | --- | --- | --- | --- |
| 1 | Cover | 35 | Deep-groove ball bearing | 69 | Tool holder |
| 2 | Deep-groove ball bearing | 36 | Needle | 70 | Bevel tool |
| 3 | Bolt | 37 | Second-class ring gear | 71 | Pull rod |
| 4 | Switch | 38 | Second-class bushing | 72 | Feed nut |
| 5 | Bearing seat | 39 | Deep-groove ball bearing | 73 | Handle |
| 6 | Bolt | 40 | Deep-groove ball bearing | 74 | Internal ring gear |
| 7 | Carbon brush | 41 | Needle | 75 | Gear |
| 8 | Carbon brush post | 42 | Machine casing upper cover | 76 | Connecting shaft |
| 9 | Engine cover | 43 | Second-class gear post | 77 | Nut |
| 10 | Engine rotor | 44 | Deep-groove ball bearing | 78 | Connecting shaft |
| 11 | Bolt | 45 | Third-class ring gear | 79 | Casing |
| 12 | Engine stator | 46 | Machine case | 80 | Universal-joint |
| 13 | Cable | 47 | Third-class gear post | 81 | Spring |
| 14 | Bearing | 48 | Key | 82 | Stop block |
| 15 | Engine gasket | 49 | Roller bearing | 83 | Spring pull pin |
| 16 | Key | 50 | Spring ring for hole | 84 | Rack |
| 17 | Bolt | 51 | Cone rolled bearing | 85 | Hanging ring |
| 18 | Slanting gear post | 52 | Bolt | 86 | Handle |
| 19 | Speed reducer | 53 | Machine casing lower cover | 87 | Deep-groove ball bearing |
| 20 | Slanting gear | 54 | Main spindle bushing | 88 | Machine post |
| 21 | Key | 55 | Roller bearing | 89 | Lifting gear |
| 22 | Slanting gear | 56 | Spring ring for hole | 90 | Thread sleeve |
| 23 | Slanting gear | 57 | Bolt | 91 | Bolt |
| 24 | Slanting gear | 58 | Main Feed spindle | 92 | Feed Handle |
| 25 | Bearing seat | 59 | Expansion disk | 93 | End cover |
| 26 | Bearing | 60 | Expanding block | 94 | Plane bearing |
| 27 | Bearing | 61 | Spring | 95 | Bearing set |
| 28 | Output shaft | 62 | Spring | 96 | Plane bearing |
| 29 | First-class bushing | 63 | Slanting block | 97 | Expansion nut |
| 30 | First-class ring gear | 64 | Expanding block | 98 | Bolt |
| 31 | Circlip | 65 | Pull rod nut | 99 | Pull rod |
| 32 | Bearing | 66 | Spring screw |  |  |
| 33 | Needle | 67 | Seat post |  |  |
| 34 | First-class planetary gear post | 68 | Tool disk |  |  |

Ordering Replacement Parts

Please use parts list provided in manual. Have part description and part number of required replacement parts to help expedite order and insure proper parts are being ordered

Or take photo with the damage parts email to us.

Warrant Information

Under the normal operation, warrant period:12 month

Contact information

Tendek Ky Finland

# Tel: +358-6-8302056

# Fax: +358-6-8302065

# Email: bernhard.store@tendek.fi

# www.tendek.fi

# Text boxes

CAUTION